## Slide 1: 2nd INTERVIEW WITH THE CUSTOMER
MEASUREMENT AND PROCESS CONTROL SYSTEMS
DIYmeteo – Meteorological station made out of waste material
Leonarda Gajdić, Tomislav Krvavica, Johannes Pelz, Tom Schwarting, Kristijan Vešligaj

## Slide 2
This presentation covers the outcomes of the second customer interview which include:
  The interview should point out whether the sources of the necessary components are accessible for the customer or not
  Our solution proposals were discussed regarding feasibility and quality
  The problems we face
   This should provide additional feedback regarding the technical, but also financial requirements and to find the most appropriate solution for the customer
INTRODUCTION

## Slide 3
Problem:
Our own capabilities to find useful electronic waste are limited
Some sensors are barely accessible (e.g. smartphone) and how to get the knowledge about the interfaces
Some sensors are only very rarely to find
Solution:
We get access to the universities resources
Asking experts: Repair shops for smartphone
In case the kids have no access to a specific type of device we will show them a way where to buy low budget sensors (<40Kn)
Issue 1: Sources of Components

## Slide 4
Problem:
Pressure sensors are difficult to get
No use of mechanical contacts to measure wind direction
How to calibrate DIY wind speed sensor
Humidity sensors are almost not available in old electronic devices
Solution:
Try to find old smartphone sensors  in case of analogue sensor easy interface  in case of digital output commercial sensor is recommended (<40 Kn)
Using an optical solution instead of meachanical: The rod has a piece of paper that has a digital coding in it, which can be read by light sensors.
Riding any kind of vehicle and taking speed or using public weather station as reference
They are available for <10Kn so. Maybe trying to digitalize wet bulb method
Issue 2: Sensors

## Slide 5
Alternatively or additionally to the humidity sensor it is possible to build a simple self-made rain sensor
This is possible by using a funnel which collects the rain in a certain area. The single rain drops gonna fall on a sensor (e.g. magnet which flips after contact or optical sensors) measuring the number of raindrops.  By measuring in a period of time it is possible to derive the intensity of rain
New Idea:
Rain Sensor