## Slide 1: PERFORMANCE SOLUTION Design of the whole system
MEASUREMENT AND PROCESS CONTROL SYSTEMS
DIYmeteo – Meteorological station made out of waste material
Leonarda Gajdić, Tomislav Krvavica, Johannes Pelz, Tom Schwarting, Kristijan Vešligaj

## Slide 2
Temperature sensor
  Thermistor SCK-083
    Sensor from power supply
CHOSEN CONCEPT/MODEL/SOLUTION/TOOL

## Slide 3
Anemometer - windspeed
  First concept
    Old dynamo from a bicycle, wooden sticks, plastic cups
CHOSEN CONCEPT/MODEL/SOLUTION/TOOL

## Slide 4
Anemometer - windspeed
  Second concept
    DC motor from an inkjet printer, bearings from power supply fan, sticks, cups
CHOSEN CONCEPT/MODEL/SOLUTION/TOOL

## Slide 5
Anemometer - windspeed
  Final concept
    Power supply fan with chopped off blades, DC motor from an inkjet printer, sticks, cups
CHOSEN CONCEPT/MODEL/SOLUTION/TOOL

## Slide 6
Wind direction
  Photodiodes with light emitters used from computer mouse
  First concept
    Spiral like piece of plastic
    Radius increases constantly
    Wind flag covers a variable number of photo diodes
    Number of diodes covered indicates the wind direction
  Final concept
    A variable number of diodes formed in circle
    Position of diode covered with wind flag indicates the wind direction
CHOSEN CONCEPT/MODEL/SOLUTION/TOOL

## Slide 7
Rain sensor
  Concept of a water wheel mill
    One half of a ping-pong ball with a little
    hole at the bottom
    Spinning speed!
CHOSEN CONCEPT/MODEL/SOLUTION/TOOL

## Slide 8
Temperature & humidity sensor
  Bought component – DHT11
  Easy to implement
  Already existing library
  If using this there is no need for creating
  temperature sensor ourselves
CHOSEN CONCEPT/MODEL/SOLUTION/TOOL

## Slide 9
Air pressure sensor
  Bought component – BMP180
  Already existing library
  Bonus assingment?
CHOSEN CONCEPT/MODEL/SOLUTION/TOOL

## Slide 10
Data representation
Web server running on ESP32
ESP32
32-bit processor 160-240 MHz
WiFi chip on board
12 bit SAR ADC, 9 channels available
2x 8-bit DACs
I2S, I2C, UART, PWM
CHOSEN CONCEPT/MODEL/SOLUTION/TOOL

## Slide 11
Web server
Using WiFi library
Parsing HTML code via serial (limits functionality)
DIY manual, students would need to enter: SSID and PW, and upload code to ESP
Designing web page left as bonus task
CHOSEN CONCEPT/MODEL/SOLUTION/TOOL